## Slide 1: SYP348293 A VMR-aided Hierarchical Federated Learning Network and Its Handover Scheme
The VRMs serve as the second aggregator in the two-tier hierarchical federated learning architecture:
First layer: VMR --- UEs, one VMR aggregation --- > k1 UE iterations:
Second layer: gNB --- VMRs, one gNB (global) aggregation --- > k2 relay aggregations
Scenario:
VMR i handover to VMR j
Problem:
t_1 --- The time for VMR to finish relay aggregation in this round, i.e., we have (k’2 < k2 ) UE iterations left
t_2 --- The time for VMR to finish k2 UE iterations in next round
t_train = t_1 +t_2
T_remain > t_train, no handover
t_1 < T_remain < t_train, handover after relay aggregation is finished in this round, VMR i send local Model to VMR j to finish the rest.
T_remain < t_1, VMR i force an aggregation and handover to VMR j , then it does what is in d)
Solution:
T_remain --- estimated VMR i stay time;
T_1 --- The time for gNB to finish global aggregation in this round, i.e., we have (k’1 < k1) relay aggregations left
T_2 --- The time for gNB to finish global aggregation in next round (k1 relay aggregations)
T_train = T_1 +T_2
If T_remain > T_train, no handover;
If T_1 < T_remain < T_train, handover after global aggregation in this round is finished
Note：all VMRs ,UEs and the gNB share the same global model at handover.
If T_remain < T_1,
Standard impact:
1. T_1, T_2 are new signalings, upload to gNB to assists handover decision at gNB，
2. The choice of k1 and k2 have impact on service continuity
SP 211648 FS_AIMLsys: WT#1.1 c. Enhancements of external parameter provisioning to 5GC (e.g. expected UE activity behaviors, expected UE mobility, etc.) based on Application AI/ML operation.
SP 211636 FS_VMR: WT#1. efficient mobility and service continuity for UE or a group of UEs to efficiently deliver data during different mobility scenarios (including mobility of the mobile base station relays).

## Slide 2: SYP348293 A VMR-aided Hierarchical Federated Learning Network and Its Handover Scheme
The VRMs serve as the second aggregator in the two-tier hierarchical federated learning architecture:
First layer: VMR --- UEs, one VMR partial aggregation --- > k1 UE iterations.
l-thUE in VMR#i: ; upload
Second layer: gNB --- VMRs, one gNB (global) aggregation --- > k2 relay aggregations
Scenario:
VMR i handover to VMR j
Problem:
Solution:
T_remain --- estimated VMR i stay time;
T_1 --- The time for gNB to finish global aggregation in this round, i.e., we have (k’1 < k1) relay aggregations left
T_2 --- The time for gNB to finish global aggregation in next round (k1 relay aggregations)
T_train = T_1 +T_2
If T_remain > T_train, no handover;
If T_1 < T_remain < T_train, handover after global aggregation in this round is finished
Note：all VMRs ,UEs and the gNB share the same global model at handover.
Standard impact:
1. T_1, T_2 are new signalings, upload to gNB to assists handover decision at gNB，
2. The choice of k1 and k2 have impact on service continuity
SP 211648 FS_AIMLsys: WT#1.1 c. Enhancements of external parameter provisioning to 5GC (e.g. expected UE activity behaviors, expected UE mobility, etc.) based on Application AI/ML operation.
SP 211636 FS_VMR: WT#1. efficient mobility and service continuity for UE or a group of UEs to efficiently deliver data during different mobility scenarios (including mobility of the mobile base station relays).

## Slide 3: SYP348293 A VMR-aided Hierarchical Federated Learning Network and Its Handover Scheme
The VRMs serve as the second aggregator in the two-tier hierarchical federated learning architecture:
Scenario:
VMR i handover to VMR j
Problem:
Solution:
T_remain --- estimated VMR i stay time;
T_1 --- The time for gNB to finish global aggregation in this round, i.e., we have (k’1 < k1) relay aggregations left
T_2 --- The time for gNB to finish global aggregation in next round (k1 relay aggregations)
T_train = T_1 +T_2
If T_remain > T_train, no handover;
If T_1 < T_remain < T_train, handover after global aggregation in this round is finished
Note：all VMRs ,UEs and the gNB share the same global model at handover.
Standard impact:
1. T_1, T_2 are new signalings, upload to gNB to assists handover decision at gNB，
2. The choice of k1 and k2 have impact on service continuity
SP 211648 FS_AIMLsys: WT#1.1 c. Enhancements of external parameter provisioning to 5GC (e.g. expected UE activity behaviors, expected UE mobility, etc.) based on Application AI/ML operation.
SP 211636 FS_VMR: WT#1. efficient mobility and service continuity for UE or a group of UEs to efficiently deliver data during different mobility scenarios (including mobility of the mobile base station relays).
Second layer: gNB --- VMRs, one gNB (global) aggregation --- > k2 relay aggregations
First layer: VMR --- UEs, one VMR partial aggregation --- > k1 UE iterations.
1. l-thUE in VMR#i,
Local update at t-th iteration --- ;
Upload to VMR#i every k1 UE iterations,
At k1s-th iteration ---
2. VMR#i,
Broadcast to UEs

## Slide 4: SYP348293 A VMR-aided Hierarchical Federated Learning Network and Its Handover Scheme
The VRMs serve as the second aggregator in the two-tier hierarchical federated learning architecture:
Scenario:
VMR i handover to VMR j
Problem:
Solution:
T_remain --- estimated VMR i stay time;
T_1 --- The time for gNB to finish global aggregation in this round, i.e., we have (k’1 < k1) relay aggregations left
T_2 --- The time for gNB to finish global aggregation in next round (k1 relay aggregations)
T_train = T_1 +T_2
If T_remain > T_train, no handover;
If T_1 < T_remain < T_train, handover after global aggregation in this round is finished
Note：all VMRs ,UEs and the gNB share the same global model at handover.
Standard impact:
1. T_1, T_2 are new signalings, upload to BS to assists handover decision at BS，
2. The choice of k1 and k2 have impact on service continuity
SP 211648 FS_AIMLsys: WT#1.1 c. Enhancements of external parameter provisioning to 5GC (e.g. expected UE activity behaviors, expected UE mobility, etc.) based on Application AI/ML operation.
SP 211636 FS_VMR: WT#1. efficient mobility and service continuity for UE or a group of UEs to efficiently deliver data during different mobility scenarios (including mobility of the mobile base station relays).
First layer: VMR --- UEs, one VMR partial aggregation --- > k1 UE iterations.
1. l-thUE in VMR#i,
Local update at t-th iteration: ;
Upload to VMR#i every k1 UE iterations:
At k1s-th iteration, the gradient is
2. VMR#i,
Partial aggregation --- , where is the set of UEs VMR#i serves;
is the number of samples at l-th UE;
Broadcast to UEs
Second layer: BS --- VMRs, one BS global aggregation --- > k2 partial aggregations.
1. VMR#i,,
Upload to BS every k2 partial aggregations:
At k2r-th partial aggregation, the gradient is
2. BS,
Global aggregation ---
Handover after global aggregation
Model same, no model transfer

## Slide 5: SYP348293 A Handover Scheme in Hierarchical Federated Learning
Filed & Solution
VMR i handover to VMR j during the local update
Problem:
T_remain --- estimated VMR i stay time;
T_1 --- The time for gNB to finish global aggregation in this round, i.e., we have (k’1 < k1) relay aggregations left
T_2 --- The time for gNB to finish global aggregation in next round (k1 relay aggregations)
T_train = T_1 +T_2
a). If T_remain > T_train, no handover;
b). If T_1 < T_remain < T_train, handover after global aggregation in this round is finished
Note：all VMRs ,UEs and the gNB share the same global model at handover.
Standard impact:
1. T_1, T_2 are new signalings, upload to BS to assists handover decision at BS，
2. The choice of k1 and k2 have impact on service continuity
Scenario:
The VRMs serve as the second aggregator in the two-tier hierarchical federated learning architecture:
First layer: VMR --- UEs, one VMR partial aggregation --- > k1 UE iterations.
1. UE#l in VMR#i,
Local update k1 times and transmit the model to VMR#i;
2. VMR#i,
Aggregate local models and broadcast to UEs
Second layer: gNB --- VMRs, one BS global aggregation --- > k2 partial aggregations.
1. VMR#i,,
Local aggregation k2 times and transmit the model to gNB
2. gNB,
Global aggregation and broadcast to VMRs
Solution:
Handover after global aggregation
Model same, no model transfer
1). extra model transfer
2). data/model poisoning between “local aggregated models”
KI#4: Enhancing External Parameter Provisioning &
KI#7: 5GS Assistance to Federated Learning Operation.