## Slide 1: SYP350091: A Split Learning (Model Splitting) Aided Federated Learning (SL-aided FL) Network
1. New network architecture
UE: User Equipment
AE: Assistant Equipment, edge, VMR, UAV, peer devices, etc
Federated Learning: Central server (gNB) + FL members
Member
Standalone: only UE
Non-Standalone: UE + AE
gNB chooses members (standalone, non-standalone, UE, AE, split point, service flow) based on:
1). The computation capability of UE and AE
2). The communication capability of UE and AE, i.e., uplink, downlink and sidelink
Exploitation of computation forces in the network (AE) via sidelink
Reduced communication cost
Enhanced data privacy (smashed data at AE, client model at UE and gNB)a
2. Benefits:
3. Standard impact:
TR22.876: Study on AI/ML Model Transfer-Phase 2
3GPP R19 WID “Study on AI/ML Model Transfer Phase 2” (S1-221225):
For Distributed Learning, controlled by network, each device uses the localized data while transfer the intermediate data to other nodes the device moves a certain coverage, has low power, or for combined computation for a big mode.
For Federated Learning, Using direct device connection can involve devices outside 5G hotspot for distributed AI training/inference, partly offload computation to neighboring device, so as to improve the training accuracy/generalization and save device power
Objective: Distributed AI training/inference based on direct device connection, e.g. traffic KPIs, different QoS and functional requirements on slidelink transmission.